## Slide 1
GIS-based Routing of Hazardous Material Cargoes Considering Incident Cost after Accidental Release of Chemicals
Bahareh Inanloo, Berrin Tansel and Xia Jin
Florida International University
Department of Civil and Environmental Engineering

## Slide 2: Hazardous Material Cargoes
More than 1 million hazardous material shipments are carried daily usually by trucks in the US.
Highway crashes involving hazardous materials have a societal cost of more than $1 billion a year.

## Slide 3: Hazardous Material Cargoes
Health impact assessment of an accidental release of gasoline compounds during transport.
Prediction of probable outcomes
  Toxic vapor cloud
Routing the hazardous cargoes in order to decrease the adverse outcomes:
  Health risk caused by toxic vapor cloud inhalation.
  Delay cost caused by the accident.
Assumptions

## Slide 4: Hazardous Cargo Characteristics
Non Pressure Cargo Tank MC 306 / DOT 406
  Oval cross section non-pressure
  Single shell aluminum construction
  9000 Gallon capacity
  Transports E 10 blend of Gasoline with full capacity
  Other assumptions:
Wind Speed (mph) | Wind direction | Temperature (F)
5 | SE | 55

## Slide 5
Origin and Destination of the Cargo
regtf
Slide 5 of 18
Destination
Origin
Origin: Port Everglades, Hollywood, FL, USA
Destination: A gas station, Downtown, Miami, FL, USA

## Slide 6: Port Everglades
Supplies about one-fifth of Florida’s energy.
Every day:
  About 12.5 million gallons of petroleum products is delivered.
  About 400,000 individual gasoline fill-ups.
Provides petroleum products to gas stations in 12 counties all over South Florida.

## Slide 7: Methodology
Routing the hazardous cargoes:
  Alternative routes identification
  Health risk calculation
  Delay cost calculation
  Comparison of the routes

## Slide 8: Risk Calculations
Risk according to DOT guideline:
    Data needed:
      Accident probability or frequency
      Accident consequences

## Slide 9: Accident Consequences, ALOHA
ALOHA (Areal Locations of Hazardous Atmospheres)
An air dispersion model able to predict airborne chemical concentrations.
Inputs:
  Wind direction
  Wind speed
  Humidity
  Date and time
  Temperature
  Location
  Chemical characteristics

## Slide 10: Accident Consequences, ALOHA
Abilities:
  Sketches the impact radius
  Has the ability to export the impact area to ArcMap and MARPLOT
  Considers urbanization of surrounding area by assigning roughness
Outputs:
    Visual expression of impacted zone

## Slide 11: Health Impact Area Delineation
Health Impact Identification
Slide 11 of 18
Routes Overall Health Impact
Impacted Population Identification

## Slide 12: Risk Calculations, Accident Frequency
Accident probability or frequency:
  Crash Rate:

## Slide 13: Crash Rate Calculations
Truck Routes
Slide 13 of 18
Annual Average Daily Traffic
Crashes
Crashes Along the Routes

## Slide 14: Delay Cost Calculations
Queuing analysis
  Is used to calculate incident delays.
  The total delay :
    Data needed:
      AADT
      Road capacity
      Capacity after accident

## Slide 15: Delay Cost Calculations
Route Capacity Calculation
Remaining capacity
Free-Flow Speed (mph) | Base Capacity (pc/h/ln)
75 | 2,400
70 | 2,400
65 | 2,350
60 | 2,300
55 | 2,250
Number of Lanes | One Lane Blocked | Two Lanes Blocked | Three Lane Blocked
2 | 0.35 | 0.00 | N/A
3 | 0.49 | 0.17 | 0.00
4 | 0.58 | 0.25 | 0.13
5 | 0.65 | 0.40 | 0.20
6 | 0.71 | 0.50 | 0.26
7 | 0.75 | 0.57 | 0.63
8 | 0.78 | 0.63 | 0.41
2200

## Slide 16: Route Comparison
Chart: Health Risk
| 7.1563086980902758E-3
Route_1 | 30.9941
Route_2 | 57.1717
Route_3 | 160.7226
Route_3
Route_1
Route_2

## Slide 17: Concluding Points and Future Works
Prediction of health risk and delay cost.
Efficiently routing hazardous material cargoes.
Future works:
  Using a Multi Criteria Decision Making method.
  Scheduling the tanker trucks.
  To provide a network of cargo routes.
  Land use specification to avoid public places.

## Slide 18: Thank you!
Questions?